## Slide 1
SWFDP and SARFFG Workshop
24 October 2016
Vanetia Phakula

## Slide 2: What is a flash flood
WMO: flood of short duration with a relatively high peak discharge.
AMS: a flood that rises and falls quite rapidly with little or no advance warning, usually as the result of intense rainfall over a relatively small area.
US NWS: a rapid and extreme flow of high water into geomorphic low-lying areas-rivers, dry lakes and basins, or a rapid water level rise in a stream or creek above a predetermined flood level.

## Slide 3: Need for flash flood forecasting
According to WMO findings, flash floods were among the top most important hazards around the world.
On average, these events kill more people worldwide than any other natural disasters

## Slide 5: SARFFG

## Slide 6: SAFFG
Interfaces

## Slide 7: Radar
The radar rainfall estimates are provided on a grid having approximately 2x2 km resolution which is displayed over a background of SAFFG sub-basin boundaries.
The radar data products are updated every hour and reflect rainfall accumulations ending on the current navigation hour

## Slide 8: Satellite
From geostationary satellites using the Hydro-estimator algorithm. The satellite rainfall estimates are provided on a grid having approximately 4x4 km resolution which is displayed over a background of SAFFG sub-basin boundaries.

## Slide 9: FFG & SARFFG (Flash Flood Guidance & South African Flash Flood Guidance System)

## Slide 10: FFG
FFG value indicates:
The total volume of rainfall over the given duration which is just enough to cause bankfull flow at the outlet of the draining stream.
Consequently, rainfall volumes of the same duration that are greater than the FFG value indicate a likelihood of overbank flows at the draining stream outlet (covered in the base line threats)
10
Templ ref: PPT-ISO-colour.001 Doc Ref no: 24/10/2016

## Slide 11: Baseline Threats

## Slide 12: IFFT
IFFT - Imminent Flash Flood Threat
The values indicate the difference of the observed mean areal rainfall of the given duration and the corresponding past FFG of the same duration for a given SAFFG sub-basin.
The last 1-hour, 3-hour and 6-hour durations of FFG are considered with current corresponding Merged MAP in the computation of IFFT.
12
Templ ref: PPT-ISO-colour.001 Doc Ref no:24/10/2016

## Slide 13
IFFTdt= MAPdt - PFFGdt
Templ ref: PPT-ISO-colour.001 Doc Ref no:24/10/2016

## Slide 14
Note that this set of products concerns the past and may not be appropriate to use for real-time warning. In addition, significant uncertainty may be associated with the estimated mean areal precipitation. IFFT is offered as a baseline product that must be carefully evaluated by the forecaster in real-time.
14
Templ ref: PPT-ISO-colour.001 Doc Ref no:24/10/2016

## Slide 15: PFFT
PFFT - Persistence Flash Flood Threat
Values indicate the difference of recent persisted merged estimates of mean areal rainfall of the given duration and the corresponding current FFG of the same duration for a given SAFFG sub-basin
15
Templ ref: PPT-ISO-colour.001 Doc Ref no:24/10/2016

## Slide 16
PFFTdt = MAPdt- FFGdt
Templ ref: PPT-ISO-colour.001 Doc Ref no:24/10/2016

## Slide 17: Hourly Rainfall Data for Gauteng 12 January 2016

## Slide 18: 06 FFG 2016/01/12 01hr

## Slide 19: 06 FFG 2016/01/12 02hr

## Slide 20: 06 FFG 2016/01/12 03hr

## Slide 21: 06 FFG 2016/01/12 04hr

## Slide 22: 06 PFFT 2016/01/12 04hr

## Slide 23: 06 FFG 2016/01/12 05hr

## Slide 24: 06 PFFT 2016/01/12 05hr

## Slide 25: 06 FFG 2016/01/12 06hr

## Slide 26: 06 PFFT 2016/01/12 06hr

## Slide 27: 06 FFG 2016/01/12 07hr

## Slide 28: 06 PFFT 2016/01/12 07hr

## Slide 29: Data used for verification

## Slide 30: Thank You